## Slide 1: Natural Neighbor Based Grid DEM Construction Using a GPU
Alex Beutel
Duke University
Joint work with Pankaj K. Agarwal and Thomas Mølhave

## Slide 2: Light Detection and Ranging (LiDAR)
Planes collect data with lasers
Each point recorded (x,y,z)
Image from USDA

## Slide 3: Flood mapping – Mandø, Denmark
90 meter grid resolution
2 meter grid resolution

## Slide 4: Digital Elevation Model (DEM)
LiDAR data is just a point cloud
Create simpler models that are easier to process
Modeled as a grid DEM
Grid requires interpolation at grid points
Used in many GIS applications
  Hydrology, contouring, noise computations, line-of sight, city planning

## Slide 5: DEM Construction
Must interpolate value at each grid point
Linear interpolation based on Delaunay triangulation [Agarwal et al. 2005]
  Simple but not smooth
  Relatively fast
Regularized spline with tension (RST) [Mitasova et al. 1993]
  Uses high-order polynomials
  Better with sparse data
  Slow

## Slide 6: Natural Neighbor Interpolation (NNI)
Voronoi diagram based
Has been used but too slow
Take advantage of general purpose graphics processing unit (GPGPU)
NNI
Linear Interpolation

## Slide 7: Our Contributions
Build high-quality, large-scale grid DEMs with a natural neighbor based interpolation scheme using the GPU
  Handle gaps in data by introducing the idea of region of influence
  Exploit the fact that we only interpolate at grid points using clever blocking. Handle 106 NNI queries in one pass. Previous maximum of ~32 [Fan et al. SIAM, 2005]
  Use CUDA to improve performance of our implementation

## Slide 8: Outline
GPU background
Voronoi diagrams on the GPU
Natural neighbor interpolation (NNI)
Batched NNI
  On grids
Implementation
Evaluation

## Slide 9: Graphics Processing Unit (GPU)
Specialized hardware for parallel processing
Render 3D objects on 2D plane of pixels Π from a viewpoint o
Used generically in other applications
  Robot collision detection, database systems, fluid dynamics

## Slide 10: GPU Buffers
Buffers are 2D array of pixels.
Store unique piece of information about each pixel
Color Buffer
  Stores information about color as seen from a given viewpoint at each pixel
  Can blend objects in line of sight
  Binary options such as bitwise-OR
Depth buffer
  Stores distance to closest object from viewpoint
  Can be set to read-only
Color Buffer

## Slide 11: GPU Model of Computation
On card memory for buffers
  Slow read-back to main CPU memory
  Fast, parallel access on card
CUDA for general purpose parallel processing
GPU
Graphics Card Memory
CPU
Main Memory
SLOW
FAST
FAST

## Slide 12: Computing the Voronoi Diagram
[Hoff, et al. 1999]

## Slide 13: Voronoi Diagram
Voronoi diagram, Vor(S), is the planar subdivision induced by the Voronoi cells of S
A Voronoi cell Vor(pi) is the region in space for which pi is the closest point (the nearest neighbor) from the set of input points S
Notes: As discussed yesterday by sarana nutanong

## Slide 14: Voronoi Diagram and Lower Envelopes
For each point pi define function
Lower envelope of {f1,f2…fn} is
Lower envelope is distance from x to its nearest neighbor

## Slide 15: Rendering the Voronoi Diagram
Render on GPU with looking at cones from below
(viewpoint at -∞)

## Slide 16: Pixelized Voronoi Diagram
Drawing on GPU discretizes Voronoi diagram. Call this PVorS(p).
Render cone for each input point
Depth buffer stores distance from the pixel to the closest input point (structure of the Voronoi diagrmam)
Color buffer can store any information specific to the closest input point
Color buffer
Depth Buffer

## Slide 17: Generating Pixelized Voronoi Diagrams
Render using truncated polyhedralcones

## Slide 18: Truncated Pixelized Voronoi Diagram TPVor(S)
Radius of cone r defines region of influence
If two points are >2r apart their cones can not overlap and they can not effect each other.

## Slide 19: Natural Neighbor Interpolation

## Slide 20: Natural Neighbor Interpolation
Vor(q) takes area from neighboring cells (natural neighbors)
Interpolate h(q) based on weighted average of heights of natural neighbors h(pi)
Weights are based on:

## Slide 21: Natural Neighbor Interpolation
|TPVor(q1)| = 73
h(q1)=(33/73)h(p1)+(12/73)h(p2)+(28/73)h(p3)
Call this process BufferAnalysis

## Slide 22: NNI Query Processing
Draw TPVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis
Main Memory
GPU Memory

## Slide 23: Batching NNI Queries
[Fan, et al. SIAM 2005]

## Slide 24: NNI Batch Query Processing
Draw TPVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis
SLOW

## Slide 25: Batching NNI Queries
For a given pixel, only need to know if Voronoi cell for q covers it (Y/N)
Only use one bit in color buffer for each query
Color buffer performs bitwise-OR

## Slide 26: NNI Batch Query Processing
Draw TPVor(S)
Save and clear color buffer
Draw Voronoi cell for 32 queries
Save color buffer
BufferAnalysis
SLOW

## Slide 27: Batching Grids of NNI Queries

## Slide 28: NNI for Grid DEM Construction
Grid of queries, M x M grid

## Slide 29: Batched NNI on Grids
w is number of bits in color buffer (and number of queries we can handle by previous algorithm)
Break grid into query blocks of size B x B
Could handle each in one pass with previous algorithm
Notes: Previous algorithm can handle up to w simultaneous queries so we break into query blocks of size <=w

## Slide 30: Batched NNI on Grids
Make assumption that cone radius is less than half the width of one query block
Queries in same position in different query blocks are independent
Execute previous algorithm on each query block simultaneously

## Slide 31: NNI Grid Query Processing
Draw TPVor(S)
Save and clear color buffer
Draw Voronoi cell for ~106 queries
Save color buffer
BufferAnalysis

## Slide 32: Larger Grids
Grids restricted by size of memory on GPU
Developed a binning procedure
  Sub-grids that can be handled by GPU
  Separate input data

## Slide 33: Putting it together

## Slide 34: Implementation
Ran on
  Intel Core2 Duo CPU running Ubuntu 10.4
  NVIDIA GeForce GTX 470 with CUDA 3.0
OpenGL
  Templated Portable I/O Environment (TPIE) for interacting with disk efficiently

## Slide 35: NNI Batch Query Processing
Draw TPVor(S)
Save and clear color buffer
Draw Voronoi cell for ~106 queries
Save color buffer
BufferAnalysis
Optimize GPU to CPU communication
  Transferring color buffers between GPU and CPU memory is slow
  For each query we have a multiple pixels
  Transferring extra data
  Perform BufferAnalysis with CUDA directly on GPU
  Only transfer one value for each query point
SLOW
SLOW
Draw TPVor(S)
BufferAnalysis
Draw Voronoi cell for ~106 queries
Save interpolated heights

## Slide 36: Tests
Denmark (DKPART):
  27 GB
  1 billion data points
  900 km2 region
Afghanistan:
  3.5 gigabytes
  186 million data points
  4 km2 region
Fort Leonard Wood (Missouri)
  57 GB
  2.2 billion data points
  600 km2 region
Source: NASA
Data from COWI A/S and the Army Research Office
Notes: LiDAR = Light Detection and Ranging

## Slide 37: Performance - Efficiency
 | Afghanistan | DKPART | Fort Leonard Wood
Size of input (106) | 186 | 1038 | 2180
Size of output (106) | 9.5 | 213 | 151
RST | 5698 | 66729 | 122305
Times in seconds

## Slide 38: Performance - Efficiency
 | Afghanistan | DKPART | Fort Leonard Wood
Size of input (106) | 186 | 1038 | 2180
Size of output (106) | 9.5 | 213 | 151
RST | 5698 | 66729 | 122305
Linear Interpolation | 962 | 7377 | 20307
Times in seconds

## Slide 39: Performance - Efficiency
 | Afghanistan | DKPART | Fort Leonard Wood
Size of input (106) | 186 | 1038 | 2180
Size of output (106) | 9.5 | 213 | 151
RST | 5698 | 66729 | 122305
Linear Interpolation | 962 | 7377 | 20307
NNI without CUDA | 1252 | 14323 | 11164
Binning Time | 91 | 569 | 1036
Interpolation Time | 1161 | 13754 | 10128
Times in seconds

## Slide 40: Performance - Efficiency
 | Afghanistan | DKPART | Fort Leonard Wood
Size of input (106) | 186 | 1038 | 2180
Size of output (106) | 9.5 | 213 | 151
RST | 5698 | 66729 | 122305
Linear Interpolation | 962 | 7377 | 20307
NNI without CUDA | 1252 | 14323 | 11164
NNI with CUDA | 163 | 1238 | 2190
Binning Time | 67 | 558 | 1030
Interpolation Time | 96 | 680 | 1160
Times in seconds

## Slide 41: Performance - Efficiency
 | Afghanistan | DKPART | Fort Leonard Wood
Size of input (106) | 186 | 1038 | 2180
Size of output (106) | 9.5 | 213 | 151
RST | 5698 | 66729 | 122305
Linear Interpolation | 962 | 7377 | 20307
NNI without CUDA | 1252 | 14323 | 11164
NNI with CUDA | 163 | 1238 | 2190
Binning Time | 67 | 558 | 1030
Interpolation Time | 96 | 680 | 1160
Times in seconds

## Slide 42: Performance - Quality
Afghanistan
all ground points
Afghanistan
sparse ground points
NNI
Linear Interpolation

## Slide 43: Future Work
NNI for grid DEMs on GPU
  Scalable
  Much faster
Make region of influence more flexible
Extend algorithm to 3D
  Spatial-temporal data

## Slide 44: Questions?
alex.beutel@cs.duke.edu
http://alexbeutel.com
Special thanks to Pankaj Agarwal and Thomas Mølhave for all their help
Thanks to COWI A/S and the Army Research Office for access to data

## Slide 45: Performance - Efficiency
 | Afghanistan | DKPART | Fort Leonard Wood
Size of input (106) | 186 | 1038 | 2180
Size of output (106) | 9.5 | 213 | 151
NNI with CUDA | 163 | 1238 | 2190
Binning Time | 67 | 558 | 1030
Interpolation Time | 96 | 680 | 1160
NNI without CUDA | 1252 | 14323 | 11164
Binning Time | 91 | 569 | 1036
Interpolation Time | 1161 | 13754 | 10128
Linear Interpolation | 962 | 7377 | 20307
RST | 5698 | 66729 | 122305
Times in seconds

## Slide 46: Performance - Efficiency
 | Without CUDA |  | With CUDA | 
Grid Resolution (m.) | 0.8 | 2 | 0.8 | 2
GPUVoronoi(S) | 411 | 73 | 76 | 74
Read C1 | 814 | 116 | N/A | N/A
Draw Query Cones | 51 | 5.84 | 39 | 6.96
Read C2 | 875 | 135 | N/A | N/A
BufferAnalysis | 102 | 9.57 | 183 | 0.46
Write Points | 4.01 | 0.92 | 4.2 | 0.8
Total | 2289 | 371 | 337 | 105
Times in seconds

## Slide 47: Performance - Efficiency
 | Without CUDA |  | With CUDA | 
Grid Resolution (m.) | 0.8 | 2 | 0.8 | 2
GPUVoronoi(S) | 411 | 73 | 76 | 74
Read C1 | 814 | 116 | N/A | N/A
Draw Query Cones | 51 | 5.84 | 39 | 6.96
Read C2 | 875 | 135 | N/A | N/A
BufferAnalysis | 102 | 9.57 | 183 | 0.46
Write Points | 4.01 | 0.92 | 4.2 | 0.8
Total | 2289 | 371 | 337 | 105
Times in seconds

## Slide 48: Voronoi Diagram
Voronoi diagram, Vor(S), is the planar subdivision induced by the Voronoi cells of S

## Slide 49: Natural Neighbor Interpolation

## Slide 50: Natural Neighbor Interpolation

## Slide 51: Truncated Pixelized Voronoi Diagram TPVor(S)
Radius of cone r defines region of influence
If two points are >2r apart their cones can not overlap and they can not effect each other.

## Slide 52: Tests
Compared against linear interpolation based on Delaunay triangulation and RST
Used w=32, 6-sided polyhedralcones, r=~20 m.
Data sets
  DKPART – 1 billion data points over 10 x 90 km of Denmark data set (courtesy of COWI A/S). 27GB
  Afghanistan – 186 million data points over 4 km2 in Paktika province (provided by ARO). 3.5 GB
  Fort Leonard Wood – 2.2 billion points over 600 km2 in Missouri (provided by ARO). 57 GB

## Slide 53: Handling Larger Grids
Algorithm is limited by size of GPU memory
Maximum size grid in one pass is μ x μ
Divide grid into sub-grids of necessary size
Using binning procedure for optimal I/O efficiency

## Slide 54: GPU Buffers
Depth buffer
  pj is intersection of ray oπ and ωj
  Can set to read-only
Color Buffer
  αj is blending parameter
  χj is color of ωj
  Binary options such as bitwise-OR
Color Buffer C

## Slide 55: Handling Larger Grids
Algorithm is limited by size of GPU memory
Maximum sized grid in one pass is N x N
Divide grid into sub-grids Q of necessary size μ x μ with μ=(N-4r/ρ)/s
Using binning procedure for optimal I/O efficiency

## Slide 56: I/O Efficient Binning
Have memory of size M and we write to disk with blocks of size B
If μ>M then m=M/μ and we need m2 sub-grids
Can hold at most M/B streams in memory (holding B points per stream in memory at a time)
Partition into groups P of Q of size n=m/(M/B)1/2
Recurse on P
Depth of recursion is O(logM/BM/μ)

## Slide 57: Handling Larger Grids
Create point stream for each sub-grid
Iterate through points
Add points to each sub-grid which the point’s cone could effect
  Within r of the sub-grid
If necessary, recurse
Run algorithm on each sub-grid Q independently

## Slide 58: BufferAnalysis
Iterate over pixels
Check if pixel is part of query point q’s Voronoi cell (color is set)
For each pixel reference C1 for height of natural neighbor from which q stole area
Set of pixels Π

## Slide 59: NNI Batch Query Processing
Draw Voronoi cell for query
Save and clear color buffer C2
BufferAnalysis
SLOW
Draw TPVor(S)
Save and clear color buffer C1

## Slide 60: NNI Query Processing
Draw TPVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis

## Slide 61: Updated BufferAnalysis
Iterate over pixels
Check if pixel π is colored
  For each bit in C2[π] that is 1 find corresponding query point qi
  Reference C1 for height
  Update interpolated height

## Slide 62: NNI Batch Query Processing
Draw Voronoi cells for 32 queries
Save and clear color buffer C2
BufferAnalysis
SLOW
Draw TPVor(S)
Save and clear color buffer C1

## Slide 63: NNI on Grids
M x M grid of query points
Spaced by ρs

## Slide 64: Batched NNI on Grids
w is number of bits in color buffer (and number of queries we can handle by previous algorithm)
Break grid into query blocks of size B x B
Could handle each in one pass with previous algorithm
Notes: Previous algorithm can handle up to w simultaneous queries so we break into query blocks of size <=w

## Slide 65: Independence
Cones can only color pixels within a radius of r
If regions of influence are disjoint (independent) can use the same color for both cones
For a given red colored pixel must be able to determine which query colored it from set {q1,q2,q3,q4}
If the queries are independent then the closest query colored it

## Slide 66: Batched NNI on Grids
Make assumption that cone radius is less than half the width of one query block
Queries in same position in different query blocks are independent
Execute previous algorithm on each query block simultaneously

## Slide 67: Updated BufferAnalysis
Iterate over pixels
Check if pixel π is colored
  For each bit in C2[π] that is 1 find corresponding set of query points Qj that used this bit as their color
  Find qi in Qj that is closest to π and update interpolated height for this query point
For red bit, Qj = {q1,q2,q3,…}
For blue bit, Qk = {q4,q5,q6,…}

## Slide 68: Implementation Optimizations
Reduce disk-transfer
  I/O efficient binning of data for large grids
  Use Templated Portable I/O Environment (TPIE)

## Slide 69: GPU Buffers
Buffers are 2D array of pixels.
Store unique piece of information about each pixel
Depth buffer
  Stores distance to closest object from viewpoint
  Can be set to read-only
Color Buffer
  Stores information about color as seen from a given viewpiont at each pixel
  Can blend objects in line of sight
  Binary options such as bitwise-OR
Color Buffer C

## Slide 70: Performing an NNI query
|TPVor(q1)| = 73
h(q1)=(33/73)h(p1)+(12/73)h(p2)+(28/73)h(p3)
Call this process BufferAnalysis