## Slide 1: TerraNNI: Natural Neighbor Interpolation on a 3D Grid Using a GPU
Alex Beutel
Carnegie Mellon University
Joint work with Pankaj Agarwal, Thomas Mølhave, Arnold Boedihardjo, James Shine

## Slide 2: Flood mapping – Mandø, Denmark
90 meter grid resolution
2 meter grid resolution
Notes: Explain importance of high-res and scalablility

## Slide 3: Change Detection – Nags Head, NC
http://skagit.meas.ncsu.edu/~helena/grasswork/NH9908p_anim.gif
Notes: Why is this important? Explain easier to obtain spatio-temporal data, change detection one possible application

## Slide 4: Change Detection – Nags Head, NC
2002-2003
2003-2004
Notes: Why is this important? Explain easier to obtain spatio-temporal data, change detection one possible application

## Slide 5: LIDAR – Light Detection and Ranging
Source: http://minnesota.publicradio.org/display/web/2008/07/09/digitalmap/

## Slide 6: Digital Elevation Model (DEM)
Geographic Information Systems need models
Enables many applications
  Hydrology, contouring, noise computations, line-of-sight, city planning

## Slide 7: GRID Terrain Models
Linear interpolation based on Delaunay triangulation [Agarwal et al. ‘05]
  Simple but not smooth
  Relatively fast
Regularized spline with tension (RST) [Mitasova et al. ‘93]
  Uses high-order polynomials
  Better with sparse data
  Slow
Natural Neighbor Interpolation (NNI) [Beutel et al. ‘10]
  Smooth, fast, and scalable
  Discretized on the GPU

## Slide 8: Voronoi Diagram in 2D
A Voronoi cell Vor(pi) is the region in space for which pi is the closest point (the nearest neighbor) from the set of input points S

## Slide 9: 2D Natural Neighbor Interpolation
Vor(q) takes area from neighboring cells (natural neighbors)
Interpolate h(q) based on weighted average of heights of natural neighbors h(pi)
Weights are based on:

## Slide 10: 3D Interpolation
For spatial-temporal data must use a volumetric grid
CPU algorithms have trouble scaling to higher dimensions
Efficiency and scalability become more important
Used in geostatistics, environmental sciences, GIS, biomedical engineering, and other disciplines
9
Notes: CRUCIAL
Multiple years of LIDAR data
Volumetric grid of form (x,y,t) with elevation z at each grid point

## Slide 11: 3D Natural Neighbor Interpolation
NNI extends to higher dimensions and a wide class of distance metrics
Our Contributions:
  TerraNNI: GPU algorithms for 3D NNI
  trade-offs in time and GPU memory
  Implementation is fast, scalable and robust

## Slide 12: Outline
GPU background
Voronoi diagrams
  Triangulation
  Lifting Transform
Fast batch NNI in 2D
NNI algorithms for 3D grids
  Slow, little memory usage
  Faster, medium memory usage
  Fastest, high memory usage
Evaluation
Notes: Remove image? Too distracting?

## Slide 13: Graphics Processing Unit (GPU)
Specialized hardware for parallel processing
Render 3D objects on 2D plane of pixels from a viewpoint o
Not just for graphics:
  Robot collision detection, database systems, fluid dynamics

## Slide 14: Computing the 3D Voronoi Diagram
[Hoff, et al. 1999]

## Slide 15: 3D Voronoi Diagram
http://www.qhull.org/html/normal_voronoi_knauss_oesterle.jpg

## Slide 16: 3D Voronoi Diagram
As before – A Voronoi cell Vor(pi) is the region in space for which pi is the near neighbor from the set of input points S
http://www.wblut.com/blog/wp-content/2009/04/voronoi3db2.jpg

## Slide 17: Pixelized 3D Voronoi Diagram
Can discretize 3D space into voxels
  Cubes of space
  Sample from center of each voxel
Define PVorS(pi) to be the set of voxels for which, from the set S, pi is closest to the center of that voxel

## Slide 18: Pixelized Voronoi Diagram
Can look at just one plane of voxels
  Time is constant in each plane
Generate each time slice separately

## Slide 19: Cylindrical Region of Influence
Notes: Is abrupt, lead in softly
Add bullet points?

## Slide 20: Truncated Pixelized Voronoi Diagram
Define TPVor(S,τ)
  Only consider points p in S for which |tp-τ| ≤ r
  For pixel v and point p, d((xv,yv),(xp,yp)) ≤ r for v to be in TPVorS(p)
    Only draw cone (or other shape representing the metric) up to radius r

## Slide 21: Voronoi Diagram and Lower Envelopes
For each point pi define function
Lower envelope of {f1,f2…fn} is
Lower envelope is distance from x to its nearest neighbor

## Slide 22: Weighted Euclidean Lower Envelope
When evaluating for only one time slice, time is constant for all points in that time slice

## Slide 23: Lower Envelope

## Slide 24: Lower Envelope – Discretized in Time & Space

## Slide 25: Triangulation of the Lower Envelope
Find height for which d(p,x)=r
Intersect shape with m equally spaced planes
Approximate intersection of each plane with the curve by a convex k-gon
Create triangles between adjacent k-gons using 2k triangles
2km triangles required per object rendered

## Slide 26: Lifting Transform for Weighed Euclidean Metric
Drawing curved surfaces requires many triangles
More efficient if we can just draw a plane
Lower envelope of g is that same as that for f
[Guibas et al. ‘85]

## Slide 27: Lifting Transform for Weighed Euclidean Metric
Only need to draw plane for each point
Can use many less triangles
Still approximate by k-gon

## Slide 28: Computing TPVor(S,τ)
Reset framebuffer
Get P={points within “r” from t=4}
Render metric for points in P
Depth and color buffers now stores TPVor(S,τ)
Call this process GVor(S,τ)

## Slide 29: Natural Neighbor Interpolation
[Fan, et al. ‘05]
[Beutel, et al. ‘10]

## Slide 30: Natural Neighbor Interpolation
Vor(q) takes area from neighboring cells (natural neighbors)
Interpolate h(q) based on weighted average of heights of natural neighbors h(pi)
Weights are based on:

## Slide 31: BufferAnalysis
4
4
4
4

## Slide 32: NNI Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis
Notes: Remove animation, collapse subsequent slides

## Slide 33: Answering Multiple Queries
[Fan et al. ‘05]
[Beutel et al ’10]

## Slide 34: NNI Batch Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis
SLOW

## Slide 35: Using Bit Tricks while Exploiting Region of Influence and Grid Structure ….
[Fan, et al. ’05]
[Beutel, et al. ‘10]

## Slide 36: NNI Grid Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for ~106 queries
Save color buffer
BufferAnalysis

## Slide 37: NNI Batch Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for ~106 queries
Save color buffer
BufferAnalysis
SLOW
SLOW
GVor(S)
BufferAnalysis
Draw Voronoi cell for ~106 queries
Save interpolated heights
CUDA
Notes: Explain what cuda is

## Slide 38: NNI in 3D

## Slide 39: Natural Neighbor Interpolation
Largely the same:
Each time slice: use 2D method

## Slide 40: NNI on N x N Grid at to
GVor(S,τ)
BufferAnalysis
Draw Voronoi cell for ~106 queries
Save interpolated heights
Loop
over τ
for
to-r ≤ τ ≤ to+r
Interpolate(Fτ,t0τ)

## Slide 41: NNI on N x N Grid at to
Loop
over τ
for
to-r ≤ τ ≤ to+r
GVor(S,τ)
Save interpolated heights
Interpolate(Fτ,to,τ)

## Slide 42: Handling N x N x N Grids

## Slide 43: r2-pass Algorithm
GVor(S,τ)
Interpolate(Fτ,to,τ)
Save interpolated heights
to-r ≤ τ ≤ to+r
GVor(S,τ)
Interpolate(Fτ,t1,τ)
Save interpolated heights
t1-r ≤ τ ≤ t1+r
…
Interpolate N x N x {to}
Interpolate N x N x {t1}

## Slide 44: Voronoi Generation Redundancy
Fτ – Framebuffer with Voronoi at time τ
r = 1.5
F0 F1 F2 F3 F4 F5 F6 F7 F8
Interpolate grid for τ = 2
F0 F1 F2 F3 F4 F5 F6 F7 F8
F0 F1 F2 F3 F4 F5 F6 F7 F8
F0 F1 F2 F3 F4 F5 F6 F7 F8
But regenerating is F2 F3 unnecessary
Interpolate grid for τ = 3

## Slide 45
GVor(S,ti+r)
Interpolate(Fτ,ti,τ)
Save interpolated heights
ti-r ≤ τ ≤ ti+r
GVor(S,ti+1+r)
Interp (Fτ,ti+1,τ)
Save interpolated heights
ti+1-r ≤ τ ≤ ti+1+r
…
Interpolate N x N x {ti}
Interpolate N x N x {ti+1}
…
r-pass Algorithm

## Slide 46: 1-pass Algorithm
Can be used if data is time series data and d(,) is the weighted Euclidean metric
Recall
Run GVor(Sτi,τi), here:
Use CUDA to shift slice times by adding appropriate ω2(τ-ti)2 term
Combine shifted slices to get TPVor(S,τ)
Perform BufferAnalysis
Notes: Expand if time

## Slide 47: Review Algorithm Trade-offs
Algorithm Number of Passes | Number of copies of Framebuffer | Triangles rendered per point | Triangles rendered per point: Euclidean metric
r2 | 1 | ~(2r)2kmn | ~(2r)2kn
r | 2r+1 | ~2rkmn | ~2rkn
1 | 2(2r+1) | ~kmn | ~kn
Algorithm Number of Passes | Number of copies of Framebuffer | Triangles rendered per point | Triangles rendered per point: Euclidean metric
r2 | 1 | ~2000n | ~16n
r | 5 | ~500n | ~4n
1 | 10 | ~250n | ~2n
Notes: Update for k=4 in the lifting transform

## Slide 48: Experiments

## Slide 49: Implementation
Hardware
  Intel Core2 Duo CPU running Ubuntu 10.4
  NVIDIA GeForce GTX 470 with CUDA 3.0
OpenGL
  Templated Portable I/O Environment (TPIE) for interacting with disk efficiently

## Slide 50: Tests
Fort Leonard Wood (Missouri)
  8.8 GB
  450 million data points
  80.5 km2 region
  Data sets from 2009, 2010
Nags Head, NC (Coastal):
  382 MB
  20 million data points
  Data sets from 1997-1999, 2001, 2004, 2005, 2007, 2008

## Slide 51: Implementation Comparison
Precision
  Our implementation is an approximation of natural neighbor interpolation
    Error introduced by region of influence, discretization, and in some cases tessellation
  Other implementations are precise
    Computationally more expensive
Degeneracies
  Many precise implementations have trouble with degenerate data (co-planar points)
  By discretizing NNI, this is not a problem in our implementation
Notes: Is co-planar data clear?

## Slide 52: Implementation Comparison
TerraNNI:
  6 minutes 32 seconds on NC Coastal (20 million input, 48 million voxels)
  26 minutes on Ft. Wood (450 million input, 4 million voxels)
Interpolate3d
  Exhausted memory and crashed after 2 hours, about halfway through constructing the Voronoi diagram
  Completes interpolating 50,000 voxels using 10 million input points in 3 hours
Cgal (Delaunay triangulation)
  NC Coastal data set in 11 minutes
  Ran out of memory and crashed on Ft. Wood data
Qhull (Delaunay triangulation)
  Ran out of memory within a couple of minutes
  Could complete 3 million points in about 3.5 minutes
Notes: Ours took 35.8 sconds to construct the voronoi diagram

## Slide 53: Performance
Tests performed on NC coastal data set
Algorithm | r2 |  | r | 
Shape Rendered | Hyperboloid | Plane | Hyperboloid | Plane
Binning Time | 17.89s | 17.53s | 13.98s | 17.2s
GVor | 8m 15s | 3m 16s | 1m 24s | 35.8s
Draw Queries | 4m 1s | 2m 26s | 3m 44s | 2m 28s
BufferAnalysis | 3m 45s | 4m 18s | 2m 45s | 3m 5s
Write output | 5.2s | 4.54s | 3.47s | 4.53s
Total time | 16m 26s | 10m 23s | 8m 11s | 6m 32s
Faster
Notes: Note increased time for buffer analysis for planes

## Slide 54: Performance
Tests performed on NC coastal data set
Algorithm | r2 |  | r | 
Shape Rendered | Hyperboloid | Plane | Hyperboloid | Plane
Binning Time | 17.89s | 17.53s | 13.98s | 17.2s
GVor | 8m 15s | 3m 16s | 1m 24s | 35.8s
Draw Queries | 4m 1s | 2m 26s | 3m 44s | 2m 28s
BufferAnalysis | 3m 45s | 4m 18s | 2m 45s | 3m 5s
Write output | 5.2s | 4.54s | 3.47s | 4.53s
Total time | 16m 26s | 10m 23s | 8m 11s | 6m 32s
Notes: Note increased time for buffer analysis for planes

## Slide 55: Performance
Tests performed on NC coastal data set
Algorithm | r2 |  | r | 
Shape Rendered | Hyperboloid | Plane | Hyperboloid | Plane
Binning Time | 17.89s | 17.53s | 13.98s | 17.2s
GVor | 8m 15s | 3m 16s | 1m 24s | 35.8s
Draw Queries | 4m 1s | 2m 26s | 3m 44s | 2m 28s
BufferAnalysis | 3m 45s | 4m 18s | 2m 45s | 3m 5s
Write output | 5.2s | 4.54s | 3.47s | 4.53s
Total time | 16m 26s | 10m 23s | 8m 11s | 6m 32s
Notes: Note increased time for buffer analysis for planes

## Slide 56: Future Work
Explore relationship between memory and time trade-offs in d-dimensions
We are open-sourcing TerraNNI for others to use
  Download it on Github:
bit.ly/TerraNNI

## Slide 57: Thanks!
Thanks to the Army Research Office for access to data

## Slide 58: NNI Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis
Main Memory
GPU Memory
Notes: Remove animation, collapse subsequent slides

## Slide 59: Natural Neighbor Interpolation
|TPVor(q1)| = 73
h(q1)=(33/73)h(p1)+(12/73)h(p2)+(28/73)h(p3)
Call this process BufferAnalysis
Discrete version:
Area of new Voronoi Cell:
Interpolated value:
Notes: Maybe make numbers big? Not sure how to not spend too much time on this
DELETE

## Slide 60: BufferAnalysis
0
0
0
0
0
Total

## Slide 61: BufferAnalysis
0
0
0
0
0
Total

## Slide 62: BufferAnalysis
1
1
1
1
4
Total

## Slide 63: BufferAnalysis
5
5
5
5
20
Total

## Slide 64: BufferAnalysis
9
9
9
9
36
Total

## Slide 65: BufferAnalysis
10
10
10
10
40
Total

## Slide 66: BufferAnalysis
10
10
10
10
40
Total

## Slide 67: BufferAnalysis
10
10
10
10
40
Total
h(q) = (10/40)h(p1) + (10/40)h(p2) +(10/40)h(p3) +(10/40)h(p4)

## Slide 68: NNI on N x N x N Grids
GPUVoronoi(S)
NNI and BufferAnalysis

## Slide 69: GPUVoronoi(S) Overlap

## Slide 70: Lower Envelope – Continuous in Time

## Slide 71: GPU Buffers
Buffers are 2D array of pixels.
Color Buffer
  Stores information about color as seen from viewpoint
Depth buffer
  Stores distance to closest object from viewpoint
Color Buffer
Notes: Keep just last part of animation

## Slide 72: Larger Grids
Grids restricted by size of memory on GPU
Use I/O-efficient partitioning
  recursion depth

## Slide 73: Performance - Efficiency
 | Afghanistan | Fort Leonard Wood
Size of input (106) | 186 | 2180
Size of output (106) | 9.5 | 151
RST | 95m | 34h
Linear Interpolation | 16m | 338m
Times in seconds

## Slide 74: Performance - Efficiency
 | Afghanistan | Fort Leonard Wood
Size of input (106) | 186 | 2180
Size of output (106) | 9.5 | 151
RST | 95m | 34h
Linear Interpolation | 16m | 338m
NNI without CUDA | 21m | 186m
NNI with CUDA | 2m 40s | 36m
Binning Time | 1m 10s | 17m
Interpolation Time | 1m 30s | 19m
Times in seconds

## Slide 75: Performance - Quality
Afghanistan
all ground points
Afghanistan
sparse ground points
NNI
Linear Interpolation

## Slide 76: Batching NNI Queries
For a given pixel, only need to know if Voronoi cell for q covers it (Y/N)
Only use one bit in color buffer for each query
Color buffer performs bitwise-OR

## Slide 77: NNI for Grid DEM Construction
Grid of queries, M x M grid

## Slide 78: Batched NNI on Grids
w is number of bits in color buffer (and number of queries we can handle by previous algorithm)
Break grid into query blocks of size B x B
Could handle each in one pass with previous algorithm

## Slide 79: Batched NNI on Grids
Assumptions:
Queries in same position in different query blocks are independent
Execute previous algorithm on each query block simultaneously

## Slide 80: Putting it together

## Slide 81: Performance - Efficiency
 | Afghanistan | Fort Leonard Wood
Size of input (106) | 186 | 2180
Size of output (106) | 9.5 | 151
RST | 95m | 34h
Linear Interpolation | 16m | 338m
NNI without CUDA | 21m | 186m
Binning Time | 1m 30s | 17m
Interpolation Time | 19m 30s | 169m
Times in seconds

## Slide 82: Voronoi Generation Redundancy
Fτ – Framebuffer with Voronoi at time τ
Δ = 3
F0 F1 F2 F3 F4 F5 F6 F7 F8
Interpolate grid for τ = 2
F0 F1 F2 F3 F4 F5 F6 F7 F8
F0 F1 F2 F3 F4 F5 F6 F7 F8
F0 F1 F2 F3 F4 F5 F6 F7 F8
But regenerating is F2 F3 unnecessary
Interpolate grid for τ = 3

## Slide 83: Digital Elevation Models
Triangular Irregular Network (TIN)

## Slide 84: GPU Buffers
Buffers are 2D array of pixels.
Color Buffer
  Stores information about color as seen from viewpoint
Depth buffer
  Stores distance to closest object from viewpoint
Color Buffer
Notes: Keep just last part of animation

## Slide 85: GPU Model of Computation
http://www.sciweavers.org/sourcecode/gts-triangulated-surface-library
Speed of processing on GPU more heavily impacted by number of triangles rather than size of each

## Slide 86: Pixelized Voronoi Diagram

## Slide 87: Lower Envelope – Discretized in Time

## Slide 88: Lower Envelope – Discretized in Time & Space

## Slide 89: Lifting Transform for Weighed Euclidean Metric
Drawing curved surfaces requires many triangles
More efficient if we can just draw a plane
Lower envelope of g is that same as that for f

## Slide 90: Review Algorithm Trade-offs
Algorithm Number of Passes | Number of copies of Framebuffer | Triangles rendered per point | Triangles rendered per point: Euclidean metric
r2 | 1 | O(r2kmn) | O(r2kn)
r | 2r+1 | O(rkmn) | O(rkn)
1 | 2(2r+1) | O(kmn) | O(kn)
For r=2, k=50, m=5, we get the following:
Algorithm Number of Passes | Number of copies of Framebuffer | Triangles rendered per point | Triangles rendered per point: Euclidean metric
r2 | 1 | O(1000n) | O(200n)
r | 5 | O(500n) | O(100n)
1 | 10 | O(250n) | O(50n)
Notes: Table with real values underneath

## Slide 91: NNI Batch Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for query q
Save color buffer
BufferAnalysis
SLOW

## Slide 92: Using Bit-Tricks….
[Fan, et al. ‘05]

## Slide 93: NNI Batch Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for 32 queries
Save color buffer
BufferAnalysis
SLOW

## Slide 94: Terrain Dynamics in North Carolina
What if we have spatial-temporal data?
  Planes scan same region different years
Want to accurately analyze terrain dynamics over time
http://skagit.meas.ncsu.edu/~helena/grasswork/NH9908p_anim.gif

## Slide 95: Outline
GPU background
Voronoi diagrams
  Triangulation
  Lifting Transform
NNI optimization in 2D
NNI algorithms for 3D grids
  r2-pass
  r-pass
  1-pass
Evaluation
NEW PIC?

## Slide 96: GPU Model of Computation
GPU
Graphics Card Memory
CPU
Main Memory
SLOW
FAST
FAST

## Slide 97: Triangulation of the Lower Envelope
Assume that d() doesn’t have cross terms between x, y, and t
General method for triangulation distance function

## Slide 98: Truncated Polygonal Hyperboloids

## Slide 99: Lifting Transform for Weighed Euclidean Metric
Images? Don’t know how to explain without math. Can talk through it slowly

## Slide 100: Rendering the Voronoi Diagram
Render on GPU with looking at cones from below
(viewpoint at -∞)

## Slide 101: Pixelized Voronoi Diagram
Drawing on GPU discretizes Voronoi diagram. Call this PVorS(p).
Render cone for each input point
Depth buffer stores distance from the pixel to the closest input point (structure of the Voronoi diagram)
Color buffer can store any information specific to the closest input point
Color buffer
Depth Buffer

## Slide 102: Generating Pixelized Voronoi Diagrams
Render using truncated polyhedralcones

## Slide 103: Truncated Pixelized Voronoi Diagram TPVor(S)
Radius of cone r defines region of influence
If two points are >2r apart their cones can not overlap and they can not effect each other.

## Slide 104: NNI Batch Query Processing
GVor(S)
Save and clear color buffer
Draw Voronoi cell for ~106 queries
Save color buffer
BufferAnalysis
Optimize GPU to CPU communication
  Transferring color buffers between GPU and CPU memory is slow
  For each query we have a multiple pixels
  Transferring extra data
  Perform BufferAnalysis with CUDA directly on GPU
  Only transfer one value for each query point
SLOW
SLOW
GVor(S)
BufferAnalysis
Draw Voronoi cell for ~106 queries
Save interpolated heights
Notes: Greatly Simplify

## Slide 105: Batching N x N Grids
Each time slice: use 2D method
Because radius is limited, we can again do entire grid at once
Handle each time slice separately

## Slide 106: Interpolate
Consider this process as a subroutine
Interpolate(Fτ,ti,τ) defined as
  Given frambuffer Fτ containing TPVor(S,τ)
  Draw hypeboloid for each query and count necessary pixels

## Slide 108: Performance
 | O(r2) | O(r) | O(r2) | O(r)
Points/Year (106) | 10 | 10 | 50 | 50
Binning Time | 2m 40s | 3m 2s | 15m 55s | 16m 17s
GPUVoronoi(S) | 18m 28s | 4m 58s | 2h 7m | 33m 18s
Draw Query Cones | 1.128s | 1.02s | 1.2s | 0.98s
BufferAnalysis | 8m 36s | 2m 11s | 8m 23s | 2m 21s
Write Points | 0.71s | 0.01s | 1.68s | 1.63 s
Total | 29m 54s | 10m 19s | 2h 31m | 52m 6s
Output grid: 200 by 200 x 8
Radius in time: 2 (each Voronoi diagram generally required 50 million or 250 million cones to be drawn)
Notes: 50 million – 11GB of data in LAS format
10 million – 2.1GB